## Slide 1: Point Cloud Processing
Ali Hosseininaveh

## Slide 2: Table of Contents
Introduction
  Typical and advance Point cloud Processing operations
PCL programming
  How to install PCL and how to use the codes
Data Storage Formats
Segmentation
Classification
Filtering
Registration
Dynamic Registration
Surface Reconstruction
Visualization and Texturing

## Slide 3: Typical Point Cloud Processing Operations
Visualization
  Simple Point Display
  TIN/DEM Display
  Intensity Textured Point Cloud
  RGB Textured Point Clouds
  Color Coding
  Image Rendering
  Video Rendering
  Zoom/Rotate/Navigate
  Cross Section and Profile Generation
  Measurements
  Primitive Fitting

## Slide 4: Typical Point Cloud Processing Operations
Segmentation
  Segmentation refers to the operation that will segment or segregate points into different groups based on characteristics without knowledge of what they really are.
  An example of segmentation could be the separation of points, based on intensity values, into low intensity, medium intensity and high intensity. Under this segmentation scheme points in each group will not necessarily share common spatial characteristics

## Slide 5: Typical Point Cloud Processing Operations
Classification
  Classification implies the separation of points into different groups or classes defined by an intrinsic or natural characteristics.
  An example of classification is the separation of the points into vegetation, building or ground classes; each of these groups implies the knowledge of its nature.

## Slide 6: Typical Point Cloud Processing Operations
Filtering
  Filtering is the removal of a set of points from the clouds based on either a segmentation or classification scheme.
  An example of a segmentation scheme based filter could be the removal of points that are below a certain height value, without considering its nature (i.e. ground or low vegetation). A classification filter could be one that removes vegetation from an urban scene on which only brick and glass is wanted.

## Slide 7: Typical Point Cloud Processing Operations
Transformation
  Rotation and Transformation [R:t]
  Cropping
  Merging
  Geo-Referencing
    A transformation in which a point cloud with coordinates in arbitrary sensor space is converted into a geodetic coordinate frame is called geo‐referencing.
Gridding and sub-sampling
  The process of converting the point cloud into a regularly spaced data set by means of interpolation is called gridding

## Slide 8: The available software for point cloud processing
QT Modeler
Pointtools
Terrasolid
MARS
Innovmetric Polyworks
Fledermaus
Lviz
Surfer
Revit
3DReshaper
Pointstream
GOM inspect
Cloud Compare
Geomagic
Meshlab
PCL
Matlab
XBIM

## Slide 9: Advanced Point Cloud Processing Data acquisition platforms (ITC)

## Slide 10: Advanced Point Cloud Processing (ITC)
Segmentation and Classification
  3D Building Modelling
  Curbstones
  Road Marking
  Poles of traffic signs and lights
  Building Façade extraction, Modelling and Texturing

## Slide 11: Advanced Point Cloud Processing (ITC)
Classification of Point clouds
  Point based vs. segment based classification
  Useful attributes to discriminate between buildings and vegetation
    Height above the ground
    Segment size

## Slide 12: Advanced Point Cloud Processing (ITC)
3D Building Modelling
  Graph matching for building reconstruction
    Point cloud segmentation
    Selecting of roof segments
    Analysing of intersected lines and edge detection on the top of buildings
    Roof Topology graph
  Automatically aligning aerial and terrestrial point cloud for 3D Building Reconstruction

## Slide 13: Advanced Point Cloud Processing (UCL)
  Interior building reconstruction from point clouds
  Data acquisition techniques (Indoor Mobile Mapping Systems (Viametris i-MMS or Zeb1, Terrestrial Laser scanner and Total Station)

## Slide 14: Advanced Point Cloud Processing (UCL)

## Slide 15: Advanced Point Cloud Processing (UCL)
Software used for semi automatic interior 3D reconstruction from point cloud
  Scan to BIM (IMAGINiT Technologies) plugged in Revit software
  Edgewise

## Slide 16: Advanced Point Cloud Processing (UCL)
A Fully automatic 3D reconstruction algorithm ( Thomson, 2016)
Libraries used for developing the algorithm:
  eXtensible Building Information Modelling (xBIM) toolkit (http://docs.xbim.net/)
  Point cloud Library (PCL)

## Slide 17: Advanced Point Cloud Processing (UCL)
The flowchart of the wall and ceiling segmentation algorithm (Thomson)

## Slide 18: Advanced Point Cloud Processing (UCL)
Flowchart of the IFC construction process (Thomson)

## Slide 19: Advanced Point Cloud Processing (UCL)
Some spatial reasoning rules for better reconstruction:
  Reject small walls
  Extend large walls
  Merge close planes with similar normal
  Reject walls with low point density

## Slide 20: Advanced Point Cloud Processing (ISPRS)
Development of new methodologies, algorithms and applications for point cloud processing
Information extraction from point clouds, including low-level feature extraction, segmentation and classification
Point cloud registration and fusion
Cloud Computing and high-performance computing for massive point cloud processing
Geospatial Big Data processing for point clouds
Point cloud rendering and streaming for massive point clouds
Point cloud processing for building information modelling (BIM)
Ubiquitous point cloud sensing